## Slide 1: A Short Intro to FIJI

## Slide 2: What are ImageJ and FIJI?
ImageJ is a Java-based, graphic user interface-based, image analysis package
FIJI (“FIJI is just ImageJ”) is a widely-use distribution of ImageJ that comes pre-packaged with a useful set of additional plugins.
Free, open-source software.
Popular platforms, both for users, and developers who create new plugins for specific purposes.

## Slide 3: Installation and startup
A portable application (you can keep it on a remote disk, or even thumbdrive)
Usually not recommended to save it in your C:\Program Files\ for permissions reasons
https://fiji.sc
https://imagej.net/software/fiji/downloads

## Slide 4: Background: What is an image?
The Golden Rule of image analysis:
Your pixel values ARE your data.
Guard them with your life.
An array of pixel values – ‘intensities’ of some measurement.
In our case, usually the photons arriving at the camera/detector; ‘brightness’

## Slide 5: Background: Thinking in pixel values in FIJI

## Slide 6: Background: Types of images and bitdepth
28 = 256, so values 0-255
216 = 65536, so values 0-65535
An RGB image takes 24bits per pixel (8-bit for each of the 3 colours)

## Slide 7: Typical examples:
Pathology slide image:
  Chromogenic staining
  Colour camera -> RGB images
Microscopic IF image:
  Fluorescence staining
  Monochrome camera -> 16-bit or 8-bit images, one per channel
Pennycuick A et al 2020
https://doi.org/10.1158/2159-8290.CD-19-1366
IDR 9846228

## Slide 8: Background: Lookup tables (LUTs)

## Slide 9: Background: Lookup tables (LUTs)
Assign LUT to current image

## Slide 10: Opening an image

## Slide 11: Adjusting the image display

## Slide 12: Things that will screw up your pixel values #1:
!
If you do click this, FIJI will explicitly warn you about what’s about to happen.
Your pixel values will be adjusted to fit the scale that you currently have visible.

## Slide 13: Adjusting the image display

## Slide 14: Thresholding

## Slide 15: Thresholding
Clicking ‘Apply’ converts the image to a binary image – pixels that were below the threshold become 0, those above it become 255 (max on 8-bit scale).

## Slide 16: Scripting in FIJI and the Macro Recorder
A premature intro – let’s leave this running in the background and come back to it later.
You’ll see code for the things we click on appear in the recorder window.

## Slide 17: Macro Recorder
This is the raw recording of a simple procedure.
Depending on what you clicked, it may need some modifications to create a useable script.

## Slide 18: Macro Recorder
A sequence of operations is now reduced to a single click.
We’ll work up this further later on.

## Slide 19: Transformations (flip, scale, etc.)

## Slide 20: Things that will screw up your pixel values #2:
Perhaps obvious, but scaling images up or down, and rotating them (except by a multiple of 90°) will cause some changes to pixel values. Pay attention to what effect any interpolation has.
2x scale-up, with interpolation
no interpolation
30° rotation, with and without interpolation

## Slide 21: Process > Math

## Slide 22: Process > Filters
Kernel: 1 1 1
0 0 0
-1 -1 -1

## Slide 23: Filtering

## Slide 24: Filtering

## Slide 25: Lesson 4: Filtering

## Slide 26: Filtering

## Slide 27: Filtering

## Slide 28: More dimensions: stacks; timelapses, etc.

## Slide 29: More dimensions: stacks; timelapses, etc.

## Slide 30: File formats: tif, jpg, proprietary formats…
Original tif
Compressed jpg – looks OK ???
Tiff is often the de facto standard for scientific images – a long-standing, highly flexible format that can accommodate many types of image (dimensions etc).
Jpg and png are more often used for consumer photos and small online images, where file size is a greater concern. But the compression of the image does not preserve data.

## Slide 31: Things that will screw up your pixel values #3:
Conversion to jpg, png etc is a LOSSY compression – your file size will be much smaller, but there’s a cost: this ‘blockiness’ around object edges is an artefact of the compression algorithm.
Often not obvious, and wouldn’t always cause a problem, but take care: any image analysis method that assumed a natural pixel distribution may run into problems.

## Slide 32: Lesson 5: Selections
Hint: right-click on these buttons for alternative tool; double-click them for options.

## Slide 33: Lesson 5: Selections
(the whole image)
Remove selection
Bring back a selection – including from a *different image*
Many tools for manipulating a selection

## Slide 34: Lesson 6: ROIs and the ROI Manager
Hint: when doing lots of ROI work, use the Ctrl+t (or just ‘t’) hotkey!

## Slide 35: Lesson 7: Measurements

## Slide 36: Lesson 7: Measurements
What actually gets measured when you hit ‘Measure’ in the ROI Manager window?
You determine this by using ‘Set Measurements’ from the result window, (also under the ‘Analyze’ menu in the main FIJI window.
(Re-run the measurements if necessary)

## Slide 37: Macros: Putting it together 2
Let’s try to make new recordings and extend our earlier macro:
  Open an image
  Duplicate it, with a new name
  Apply a useful filter
  Set a threshold and convert to binary
  Save this binary image (so we have a record of the objects we measured)
  Run Analyze Particles… to create ROIs from the binary image
  Take those ROIs back to the original image, and Measure them to get intensities
  Save the results table

## Slide 38: Macros: Putting it together 2
Use + to concatenate strings
Go back to the original image before measuring
Magic #@ lines create dialog box to get files, folders etc

## Slide 39: Scale bars and other annotations
Adding a scale bar is easy if your image is already calibrated.
  But check that the metadata that has come in from the microscope is correct!
If the scale information isn’t there, add it either:
  manually by adding the pixel width in
  Image > Properties, or,
  By using Analyze > Set Scale… and measuring from a known-size object in the image

## Slide 40: Scale bars and other annotations

## Slide 41: Lesson 9: Overlays in general
These function in much the same way as ‘layers’ in many image-editing programs, allowing you to hold objects above the pixel data itself, non-destructively.
You can then ‘flatten’ them down onto the image when finished, ready to export it.
Interconvertible with ROIs
Scale bars, text boxes, etc can all be managed as overlays

## Slide 42: Macro Scripting: Resources
https://github.com/BiAPoL/imagej-macro-cheat-sheet/blob/master/ImageJ_macro_cheatsheet.pdf

## Slide 43: Macro Scripting: Resources
https://github.com/BiAPoL/imagej-macro-cheat-sheet/blob/master/ImageJ_macro_cheatsheet.pdf

## Slide 44: Macro Recorder to Script
Trying to re-run this straight out of the box caused this error.
Let’s troubleshoot…

## Slide 45: Macro Recorder to Script
Don’t need to select the window if it’s the only image open
These were just from clicking different threshold algos, we can get rid
This run(“Close”); line is the problem – when using the GUI, an options window was open which I manually closed – this was logged in the recorder!

## Slide 46: Limitations of FIJI: when to use something else
Very large 2D images, e.g. whole slidescans, TMAs (white-light, or fluorescence) – better off in HALO (commercial – see the Histo core) or QuPath (FOSS)
3D visualisation, processing and stitching – often better off in Imaris, or Arivis Vision4D (Microscopy core holds licences for both of these, commercial)
Some modern machine learning packages are not so easy to integrate into a Java-based platform such as FIJI, and so users are pushed elsewhere.